Tom Murray
netid: tmurray5
Descriptions of Highlighted Blocks

notGate: This component takes its input and inverts it.

ANDgate, hitDetector, missDetector: This component takes its inputs and “and”s them together. I didn't do components for all of my AND gates, but hitDetector and missDetector are also AND gates.

Orgate: This component takes its two inputs and “or”s them together.

ADDR_SPLITTER: This block takes the ADRESS input and splits the high 9 bits as the tag, the middle 4 bits as index, and the low 3 bits as offset.

Way: This hierarchical component houses 4 store RAMs. These RAMs are Data, Tag, Valid, and Dirty. Each RAM has eight data lines which are chosen based on the index signal. Each RAM also has its own data inputs. The way also takes in a DataWrite signal which drives when each of the RAMs is written to.

TagComparator: This component is essential just an 'if' statement that compares the output tag from one of the way;s to the tag signal generated by the ADDR_SPLITTER.

CheckValid: This component is almost identical to the tagComparator except that it only compares std_logic signals and not tag signals. This compoenet is an 'if' statement comparing one of the way's valid outputs to the output from tagComparator output.

CheckAccess: This block operates as a 3 to 1 nand gate.

DelakClk: This block calculates the hitGate signal. This block is like a 2 to 1 and gate. The inputs of the gate are the clock signal delayed by 34 ns and the clock signal inverted.

Delay: This component takes its input and delays it by 1 ns. This helped to fix some of my timing errors.

AddrJoiner: This block takes one of the way Tag outs and the index signal and concatnates them into a word. The offset 4 bits are all set to zeros.

LineSplitter: This block takes a 128 bit data word and splits it into 8 lc3b_words.

LineJoiner: This block takes 8 lc3b_words and concatnates them into a 128 bit data word.

WriteDecoder: This block is a 3 to 8 decoder. It uses the upper 3 bits of offset to select which word in a data line is to be written to.

Writer: This heirarchical component is used to write to a cache line.

HighLow: This component splits the 16 bit input into its 8 high bits and 8 low bits.

ByteCombiner: This block concatnates two 8 bit inputs to make an lc3b_word.